## Slide 1: Autonomous Green House Control System

## Slide 2: Group members
Saad Mohammed
Mostafa Mohammed
Youssef Hamad
Mostafa Mahmoud
Mohammed Tharwat
Mostafa Essam

## Slide 3: Why this project ?
Greenhouses are important in Egypt due to the country's arid climate, limited water resources, and high population growth, they offer a means of improving crop yields, reducing resource consumption, and providing food security for the growing population.

## Slide 4: Timeline

## Slide 5: Project main goal
The main goal of this project is to develop a smart greenhouse
system to help users optimize crop growth by monitoring and
controlling environmental factors.

## Slide 6: Project features
1- Automated control: The system uses actuators. such as fans, heaters, and
pumps, to automate controlling of the environment
2- Environmental monitoring: The system uses a network of sensors to monitor
environmental factors such as temperature, humidity, and soil moisture in real-
time and show data on an LCD screen.
3- Remotely monitoring: the system
will send the status of the greenhouse
to an IOT server.

## Slide 7: System Flowchart

## Slide 8: Project prototype

## Slide 9: Hardware
Microcontrollers
1-STM32F401CCU6
2-Raspberry Pi 3 Model B+
3- Node Mcu

## Slide 10: Hardware
Sensors
1- DH11 sensor
2-Soil Moisture Sensor
3-water level sensor

## Slide 11: Hardware
Actuators
1-12v Pump
2- 12v fan
3- 5v heating pad

## Slide 12: Hardware
4- PCB

## Slide 13: Software
  Three programming languages were used.
  1- C language.
Used to configure STM32F401CCU6 to automate the process and send the data to GUI, IOT systems.
FreeRTOS was used as an operating system.

## Slide 14: Software
2-Python
Used to create the GUI system and update data shown by GUI periodically.

## Slide 15: Software
3- Arduino C
Set up node MCU to handle communication between STM32F401CCU6 and IOT server.

## Slide 16: Future work
Add manual mode for the user to control fans, water pump and heaters.
Add mode for the user to change the system configurations.
Make these modes available to use through GUI screen and IOT application.

## Slide 17: Test cases
To see test cases press here

## Slide 18: Demo video
To see demo video press here

## Slide 19: THANKS